## Slide 1: AASHTOWare Bridge Design & Rating (BrDR) 3D FEM Analysis Troubleshooting
AASHTOWare RADBUG Meeting
July 30-31, 2019
South Lake Tahoe, CA

## Slide 2: BrDR 3D FEM Analysis Troubleshooting
Hardware recommendations
Factors that influence analysis speed
Tips for successful analysis
Troubleshooting
  Non-zero moments at end supports
  Different number of nodes per girder

## Slide 3: Hardware Recommendations
Machine: Intel Core i7 processor or equivalent
Memory: 32 GB or more
Hard Disk: Solid State Drive

## Slide 4: Factors that Influence 3D Analysis Speed
Number of degrees of freedom
Number of live load vehicles
Live loading increments
Analysis output selections

## Slide 5: Number of Degrees of Freedom
Number of shell elements in the deck between girders or in the web between flanges
Target aspect ratio for shell elements
Found on Superstructure Definition: Analysis tab

## Slide 6: Live Loading Increments
Vehicle increment for longitudinal loading
Vehicle increment in lane and lane increment for transverse loading
Found on Superstructure Definition: Analysis tab

## Slide 7: Analysis Output Selections
Choose a local folder as the Analysis Output Folder. Writing analysis output to a network folder will degrade the performance of the analysis.

## Slide 8: Analysis Output Selections
Select only the necessary analysis output for the analysis. Disk operations are expensive from the analysis performance perspective.

## Slide 9: Tips for Successful Analysis
Fine tune the model while running the DL only

## Slide 10: Tips for Successful Analysis
Review the DL model with Model Viewer

## Slide 11: Tips for Successful Analysis
Check the moments to see if they look ‘normal’
Run coarser meshes initially and only then fine tune the model

## Slide 12: Tips for Successful Analysis
Do first spec check of 1 girder only
  Launch 3D analysis from the member alternative
  Only “Existing” alternatives have influence surfaces loaded and are spec checked
Do initial live load analysis for a single vehicle only

## Slide 13: Tips for Successful Analysis
Do not select diaphragms for spec checking until satisfied with girders

## Slide 14: Troubleshoot Non-Zero Moments at End Supports
Evaluate “Pinned” support conditions

## Slide 15: Troubleshoot Different Number of Nodes

## Slide 16: Troubleshoot Different Number of Nodes
“3DGirderNodes.txt”
  Comma delimited file contains node locations and reason why node was generated
  Developed for debugging, now shared with users
6.8.3: File generated when unable to generate mesh
6.8.4/7.0.0: File always generated

## Slide 17: Troubleshoot Different Number of Nodes
Reasons why node was generated
  Diaphragm, support, tenth point, cross section change point
  “bitmask 0” : node was added to either get the same number of nodes in a span or added based on the number of shell elements selected on the Structure Definition: Analysis tab

## Slide 18: Troubleshoot Different Number of Nodes

## Slide 19: Troubleshoot Different Number of Nodes

## Slide 20: Troubleshoot Different Number of Nodes
Step 1: Use Paste/Use Text Import Wizard to copy each girder’s data into its own column in Excel

## Slide 21: Troubleshoot Different Number of Nodes
Step 2: Examine total number of nodes per girder looking for differences

## Slide 22: Troubleshoot Different Number of Nodes
Step 3: For girders with difference, examine number of nodes per spans

## Slide 23: Troubleshoot Different Number of Nodes
Diaphragm at 70.536605’ (support 2) + 259.018115’ = 329.55472’
Pier 4 is at 329.650012’

## Slide 24: Troubleshoot Different Number of Nodes
Change the number of diaphragm spacing from 15 to 14
Add a new row at 0’ from Support 5(Pier 4) with 0’ spacing
Move Span 5 data down a row

## Slide 25: Troubleshoot Different Number of Nodes

## Slide 26
Thank You