## Slide 1
Manitoba Infrastructure and Transportation RADBUG - August 2014
Water Management and Structures

## Slide 2
Innovative Overload Permitting in Manitoba Allowing a 363 250 Kg (800,830 LB) G.V.M. “Superload”
Presented by:
Geoffrey C. Oramasionwu, M.Eng., P.Eng.
Manitoba Infrastructure and Transportation RADBUG - August 2014
Water Management and Structures

## Slide 3
Manitoba Infrastructure and Transportation RADBUG - August 2014
Water Management and Structures
INTRODUCTION
  Increased demand to haul heavier loads
Many structures nearing the end of their Service Life
Increasing number of overload permit applications
MIT uses the AASHTO LRFD and LRFR Specifications for Design and Load Rating
AASHTOware Bridge Rating Program uses a refined
rating method
This AASHTOWare Bridge Rating enabled MIT to review and approve a 363, 250 Kg (800830 LB) overload

## Slide 4
Manitoba Infrastructure and Transportation RADBUG - August 2014
Water Management and Structures
THREE TRANSFORMERS, EACH WEIGHED IN AT GVM =175,450 kg (386,800 lbs)
The Overload Permit

## Slide 5
Manitoba Infrastructure and Transportation RADBUG - August 2014
Water Management and Structures
Two self propelled units
Dual 20-line hydraulic trailer units
16 tires per axle
GVM = 363,250 kg (800,830 lbs)
Total length = 34 m (110ft Approx.)
Total height = 7.435 m (24ft)
Total width = 7.55 m (24.77ft)

## Slide 6
Manitoba Infrastructure and Transportation RADBUG - August 2014
Water Management and Structures
Water Management and Structures reviewed three different truck configurations and three different routes before approving the permit application.
ROUTE OPTIONS

## Slide 7
Precast Prestressed Concrete I Girder
Designed and built id 1975 for AASHTO HS25 Truck Live Load
In composite action with a 200 mm (8 in) reinforced concrete deck
Seven simply supported spans. Span length = 36.576 m (120 ft)
Manitoba Infrastructure and Transportation RADBUG - August 2014
Water Management and Structures
Red River Bridge

## Slide 8
12 m (40 ft) Precast Pre stressed Concrete Channel Girder
100 mm (4 in) thick asphalt overlay wearing surface
Five simply supported spans. Span length = 11.8 m (38.74 ft)
Manitoba Infrastructure and Transportation RADBUG - August 2014
Water Management and Structures
ST ADOLPHE COULEE BRIDGE

## Slide 9
BRIDGE LOAD RATING
Manitoba Infrastructure and Transportation RADBUG - August 2014
Water Management and Structures

## Slide 10
NUMBER OF AXLES = 20
AXLE SPACING = 1.5 m
LONGITUDINAL CONFIGURATION DEFINITION
Manitoba Infrastructure and Transportation RADBUG - August 2014
Water Management and Structures

## Slide 11
TRANSVERSE CONFIGURATION OF A NON-STANDARD GAGE
8 WHEELS PER AXLE
VARIABLE WHEEL SPACING
Manitoba Infrastructure and Transportation RADBUG - August 2014
Water Management and Structures

## Slide 12
LONGITUDINAL FOOTPRINT OF TRUCK
OUTPUT OF VEHICLE PLAN
Manitoba Infrastructure and Transportation RADBUG - August 2014
Water Management and Structures

## Slide 13
OUTPUT OF VEHICLE AXLE PLAN (AXLE 1)
Manitoba Infrastructure and Transportation RADBUG - August 2014
Water Management and Structures

## Slide 14
ACTUAL CROSS-SECTION OF THE BRIDGE
BRIDGE DECK IS MODELED AS SHELL ELEMENTS WITH MATERIAL PROPERTIES BEING THE SAME AS THE BRIDGE DECK
Manitoba Infrastructure and Transportation RADBUG - August 2014
Water Management and Structures

## Slide 15
FINITE ELEMENT MODELING
CORE ELEMENT DATA CREATED IN “BrRAT” BRIDGE WORKSPACE WERE EXPORTED TO THE STAAD ENGINE
STAAD USES THE INFORMATION TO CREATE THE FINITE ELEMENT MODEL FOR THAT STRUCTURE
DECK SLAB  SHELL ELEMENTS
BEAM  INFINETELY STIFF MEMBERS
Manitoba Infrastructure and Transportation RADBUG - August 2014
Water Management and Structures

## Slide 16
A UNIT LOAD IS APPLIED AT EACH NODE OF THE SHELL ELEMENTS
Bending Moment, Shear Force and
Displacement Envelopes are generated for the Unit Load placed on at each element nodes.
STAAD THREE DIMENTIONAL VIEW OF THE MODEL
Manitoba Infrastructure and Transportation RADBUG - August 2014
Water Management and Structures

## Slide 17
Manitoba Infrastructure and Transportation RADBUG - August 2014
Water Management and Structures

## Slide 18
Manitoba Infrastructure and Transportation RADBUG - August 2014
Water Management and Structures

## Slide 19
3D Stress Influence Surface for the unit Load Case No. 12, Placed at a Shell Node.
Manitoba Infrastructure and Transportation RADBUG - August 2014
Water Management and Structures

## Slide 20
Manitoba Infrastructure and Transportation RADBUG - August 2014
Water Management and Structures

## Slide 21
Manitoba Infrastructure and Transportation RADBUG - August 2014
Water Management and Structures

## Slide 22
STAAD THREE DIMENTIONAL VIEW OF THE MODEL
Manitoba Infrastructure and Transportation RADBUG - August 2014
Water Management and Structures

## Slide 23
3D Stress Influence Surface for the unit Load Case No. 6, Placed at a Shell Node.
Manitoba Infrastructure and Transportation RADBUG - August 2014
Water Management and Structures

## Slide 24
 | RED RIVER BRIDGE RATING FACTORS |  |  |  |  | 
 | GIRDER | LIMIT STATE | CHBDC | AASHTO STANDARD Single/two or more Lanes | AASHTO LRFD Single/Multi-Lanes | FINITE ELEMENT MODEL
 | 1 | Shear | 0.614 | 0.390/0.390 | 0.468/0.429 | 0.131
 |  | Moment | 0.567 | 0.390/0.390 | 0.468/0.429 | 0.131
 | 2 | Shear | 0.614 | 0.98/1.24 | 0.633/0.731 | 0.207
 |  | Moment | 0.525 | 0.98/1.24 | 0.436/0.622 | 0.207
 | 3 | Shear | 0.614 | 0.98/1.24 | 0.633/0.731 | 0.221
 |  | Moment | 0.525 | 0.98/1.24 | 0.436/0.622 | 0.221
 | 4 | Shear | 0.614 | 0.98/1.24 | 0.633/0.731 | 0.231
 |  | Moment | 0.525 | 0.98/1.24 | 0.436/0.622 | 0.231
 | 5 | Shear | 0.614 | 0.85/0.85 | 0.582/0.619 | 0.223
 |  | Moment | 0.567 | 0.85/0.85 | 0.582/0.619 | 0.223
Manitoba Infrastructure and Transportation RADBUG - August 2014
Water Management and Structures

## Slide 25
ST. ADOLPHE COULEE BRIDGE RATING FACTORS |  |  |  |  | 
GIRDER | LIMIT STATE | CHBDC | AASHTO STANDARD Single/two or more Lanes | AASHTO LRFD Single/Multi-Lanes | FINITE ELEMENT MODEL
1 | Shear | 0.400 | 1.00/1.00 | 0.60/0.60 | 0.055
 | Moment | 0.339 | 1.00/1.00 | 0.60/0.60 | 0.055
2 | Shear | 0.400 | 0.56/0.72 | 0.60/0.60 | 0.172
 | Moment | 0.345 | 0.56/0.72 | 0.325/0.325 | 0.172
3 | Shear | 0.400 | 0.56/0.72 | 0.60/0.60 | 0.180
 | Moment | 0.345 | 0.56/0.72 | 0.325/0.325 | 0.180
4 | Shear | 0.400 | 0.56/0.72 | 0.60/0.60 | 0.089
 | Moment | 0.345 | 0.56/0.72 | 0.325/0.325 | 0.089
5 | Shear | 0.400 | 0.56/0.72 | 0.60/0.60 | 0.089
 | Moment | 0.345 | 0.56/0.72 | 0.325/.0325 | 0.089
6 | Shear | 0.400 | 0.56/0.72 | 0.60/0.60 | 0.180
 | Moment | 0.345 | 0.56/0.72 | 0.325/.0325 | 0.180
7 | Shear | 0.400 | 0.56/0.72 | 0.60/0.60 | 0.172
 | Moment | 0.345 | 0.56/0.72 | 0.325/.0325 | 0.172
8 | Shear | 0.400 | 1.00/1.00 | 0.60/0.60 | 0.055
 | Moment | 0.339 | 1.00/1.00 | 0.60/0.60 | 0.055
Manitoba Infrastructure and Transportation RADBUG - August 2014
Water Management and Structures

## Slide 26
Chart: For Red River Bridge
| CHBDC | AASHTO Standard Single Lane | AASHTO Standard Multi Lane | AASHTO LRFD Single Lane | AASHTO LRFD Multi Lane | Finite Element Model
Interior Girder Shear | 0.614 | 0.98 | 1.24 | 0.633 | 0.731 | 0.207
Interior Girder Moment | 0.567 | 0.98 | 1.24 | 0.436 | 0.622 | 0.207
Interior Girder Moment
Exterior Girder Shear | 0.614 | 0.39 | 0.39 | 0.468 | 0.468 | 0.131
Exterior Girder Moment | 0.567 | 0.39 | 0.39 | 0.429 | 0.429 | 0.131
Manitoba Infrastructure and Transportation RADBUG - August 2014
Water Management and Structures
RATING FACTORS FROM DIFFERENT CODES

## Slide 27
Chart: St. Adolphe Coulee Bridge
| CHBDC | AASHTO Standard Single Lane | AASHTO Standard Multi Lane | AASHTO LRFD | Finite Element Model
Interior Girder Shear | 0.4 | 0.56 | 0.72 | 0.6 | 0.089
Interior Girder Moment | 0.345 | 0.56 | 0.72 | 0.325 | 0.089
Interior Girder Moment
Exterior Girder Shear | 0.4 | 1 | 1 | 0.6 | 0.055
Exterior Girder Moment | 0.339 | 1 | 1 | 0.6 | 0.055
Manitoba Infrastructure and Transportation RADBUG - August 2014
Water Management and Structures
RATING FACTORS FROM DIFFERENT CODES

## Slide 28
LOAD RATING IS CARRIED OUT USING THE CONVENTIONAL BRIDGE RATING PROCEEDURES AS DESCRIBED EARIER
IT CAN BE SEEN THAT THIS SUPERLOAD WOULD NOT HAVE BEEN APPROVED IF WE HAD USED THE CONVENTIONAL DISTRIBUTION FACTOR CALCULATION METHOD.
Manitoba Infrastructure and Transportation RADBUG - August 2014
Water Management and Structures
RATING FACTORS FROM DIFFERENT CODES

## Slide 29
PORTABLE SCALES
Manitoba Infrastructure and Transportation RADBUG - August 2014
Water Management and Structures
WE ALSO NEEDED TO VERIFY THAT OUR MODEL IS CORRECT BY DOING SOME MEASUREMENTS DURING ONE OF MOVES.
RATING FACTORS FROM DIFFERENT CODES

## Slide 30
Travel from 8:00 pm – 6:00 am
10 km/h maximum speed
Traveling on centreline of bridge
Police escort inside the city limits and Manitoba
Compliance Officers for traffic control.
Total move – three nights
Manitoba Infrastructure and Transportation RADBUG - August 2014
Water Management and Structures
Permit Conditions

## Slide 31
Instrumentation and Data Collection
Manitoba Infrastructure and Transportation RADBUG - August 2014
Water Management and Structures
Notes: Due to accessibility reasons, the focus for the instrumentation was the PPCC structure.
As can be seen from the distribution factors from the previous slides and the transverse wheel spacing shown here; we note that girder lines G2 and G7 experienced more of the live load.
Instrumentation Placement
A telescopic measuring pole was used to manually verify the deflection in order to ensure the accuracy of the LVDT measurements
Data collection and storage was facilitated by 2 Model P3 Strain Indicator and Recorder Units with two separate laptops.

## Slide 32
Instrumentation and Data Collection
Manitoba Infrastructure and Transportation RADBUG - August 2014
Water Management and Structures
Notes: As this was undertaken during a typical MB winter, there were numerous environmental and climatic challenges to overcome.
Hoarding was constructed for the full width of the structure, beneath the mid-span of Span 1 and heat was provided.
Both the ambient air temp. and the girder concrete temperature were monitored during the installation of the instrumentation and the move. The temperatures remained relatively constant and within the allowable operating temperature of the instruments.

## Slide 33
Manitoba Infrastructure and Transportation September 2013
Water Management and Structures
Instrumentation and Data Collection
Notes: From Table 3 & 4 it is evident that the measured deflections are considerably less than those calculated from the analysis. In fact, for both structures the actual deflections represent approximately 1/3 of the theoretical deflections.
Although further testing would be required to ensure the accuracy of the measured data, you may note that the values obtained by both the LVDTs and the telescopic measuring pole do coincide.
The differences in deflection values can partially be due to subtle differences in the theoretical model versus the actual structure, such as in-situ material properties versus the design properties utilized for the load rating model. Understandably so, the load rating model also incorporates a certain level of conservatism due to material and load resistance factors to ensure an adequate amount of reserve capacity is available in the structure.
IN CONCLUSION, when NSG trucks are used for large moves, the Rigorous Method could be used to more accurately determine the effects of the load on the structure and permit a load otherwise unable to be permitted using conventional methods..

## Slide 34
Manitoba Infrastructure and Transportation RADBUG - August 2014
Water Management and Structures
Instrumentation and Data Collection